## Slide 1: SoC final project
team 7
R12943006 謝郡軒 R12943012 蔡東翰 R12943031 李允恩

## Slide 2: Block Diagram

## Slide 3: FIR
CPU
FIR
DMA
wishbone
signals
clk
rst
ap_start
indata
(axi-stream)
outdata
(valid/data)
Block diagram
FIR module
data bram (16)
tap bram (11)
*
+
axi_lite

## Slide 4: FIR
Use only 1 multiplier and 1 adder.
CPU first sends coefficients, and FIR saves coefficients in BRAM. After that, DMA sends input data
FIR receive a new data when previous answer is outputed
FIR produces 1 data per 12 cycles
If DMA is fast enough to send and receive the input/output data, the FIR process in our design totally costs about 132 cycles (excluding coef receiving time).
Our work

## Slide 5: Matmul
CPU
matmul
DMA
wishbone
signals
clk
rst
ap_start
indata
(axi-stream)
outdata
(valid/data)
A1
B1
* A1
B1
* A5
A2
B1
* A9
B1
* A13
B2
* A1
B2
* A5
B2
* A9
B2
* A13
B16
* A4
B2
* A8
A16
…
B1
B2
* A12
B2
* A16
INPUT
MULTIPLIER
B2
add to
C1
add to
C5
add to
C9
add to
C13
add to
C2
add to
C6
add to
C10
add to
C14
add to
C4
add to
C8
add to
C12
add to
C16
C1
C2
C16
…
Schedule
Block diagram
ADDER
OUTPUT
input
buffer
………
B16
matmul module
input array (16)
output array (16)
*
+

## Slide 6: Matmul
Use only 1 multiplier and 1 adder.
After we read the 4*4 A matrix, we read the elements in B matrix one by one and calculate all the results related to the current B element before asking for the next B element, we don’t need to save the whole B matrix in our design so therefore we can save about 14 registers.
If DMA is fast enough to send and receive the input/output data, the matrix multiplication process in our design totally costs about 16 (receiving A) + 64 (receiving B and calculating C) + 16 (returning C) = 96 cycles.
Our work

## Slide 7: “Quick” insertion sort
Block diagram
Schedule
CPU
sort
DMA
wishbone
signals
clk
rst
ap_start
indata
(axi-stream)
outdata
(valid/data)
input
buffer
sort module
X1
insert
X1
INPUT
INSERTION
OUTPUT
X2
insert
X2
X3
insert
X3
………
X16
insert
X16
Y1
Y2
…
Y16
X4
insert
X4
output
array
comp
start / end

## Slide 8: “Quick” insertion sort
Our work
use only 1 comparator
although quicksort may be more efficient and powerful in C++, however, in this project, we use verilog code for coding and the input sequence comes in serial, so we think using insertion sort will be more suitable.
because insertion sort is also in-place, we can use about only 12 registers to sort 10 elements (2 more for buffering)
If DMA is fast enough to send and receive the input/output data, the insertion sort process in our design totally costs about 53 cycles.

## Slide 9: UART
Block diagram
UART
uart_ctrl
uart_rx
uart_tx
rx buffer
tx buffer
rx signals
tx signals
count-down
counter
rx counter
user_irq
wishbone decoder
wishbone signals

## Slide 10: UART
Our work
We add buffers at both rx and tx sides, so that (1) we don’t need to enter ISR as soon as one interrupt happens, and (2) we can send another data to be transmitted without waiting for the previous one to finish its transmission.
Besides, to prevent unsettled interrupts, we have a count-down counter to check if the rx buffer is empty periodically.
Therefore, we can set two parameters n and m, which the UART generates an irq signal if there has been total n unsettled interrupts or m cycles since the last time entering ISR.

## Slide 11: Direct Memory Access
Block diagram

## Slide 12: Direct Memory Access
Our work
There are 3 DMAs for FIR, MM, and QS respectively.
Each of them will receive five data through axi-lite protocol from CPU, including information of data_len, data_addr, ans_len, ans_addr, ap_start, and DMAs have to return the ap_done signal back to CPU when necessary.
After receiving all data above, DMAs will ask for input data for FIR/MM/QS engines through wishbone protocol from SDRAM controller according to the given data_addr and data_len, and save them into DATA BRAM in order.
However, we need an arbiter between DMAs and SDRAM controller to avoid collision of data requests.

## Slide 13: Direct Memory Access
Our work
After saving all input data into DATA BRAM, DMAs will start sending input data into FIR/MM/QS engines through axi-stream protocol with a view to activating the corresponding computations.
When FIR/MM/QS engines finish the operations, they will send the answers back to DMAs through axi-stream protocol, which will be saved in ANS BRAM in order by DMAs.
After saving all answer data into ANS BRAM, DMAs will start sending answer data to arbiter through wishbone protocol. Eventually, arbiter and SDRAM controller will save those data into SDRAM properly.

## Slide 14: Arbiter
Block diagram
FIR
DMA
Arbiter
SDRAM controller
wishbone signals
wishbone signals
wishbone signals
wishbone signals
selector
matmul
DMA
sort
DMA
CPU
wishbone signals
FIFO

## Slide 15: Arbiter
Our work
Arbiter collects the wishbone signals of DRAM access from 3 DMAs and CPU together, putting them in a FIFO, and then arbiter will access the DRAM according the output of FIFO and send back the corresponding wishbone signals to DMA.
Since wishbone signals cannot be pipelined, arbiter will receive a new request from one source only when the last request from the same source has been fulfilled. Therefore, we only need a FIFO of size 4 to accommodate all the requests from 4 different sources.
To accelerate the whole process, if two requests comes in at the same time, the priority will be CPU > FIR > matmul > sort

## Slide 16: SDRAM controller
Block diagram
FSM (our different part)
Arbiter
SDRAM controller
SDRAM
wishbone signals
SDRAM signals
FSM
cache 0
cache 1
IDLE
READ
WAIT
READ_RES
data is in cache
data is not in cache
wait for 3T
receive data
from SDRAM
fetch data
prefetch data
of (addr + 8)

## Slide 17: SDRAM controller
Schedule
Data is in cache
Data isn’t in cache

## Slide 18: SDRAM controller
Our work
We observe that if this cycle CPU is accessing address “x” then the next cycle CPU will likely access address “x+4”.
Since it costs 3 cycles from we send a request to SDRAM to we get the data, we need to have at least 2 caches to store the prefetch datas.
Therefore, we use 2 caches where cache n (n = 0, 1) saves the data whose addr[2] == n, and every time we send back a data of address “x” to arbiter we will immediately go prefetch the data of address “x+8” and save it in the corresponding cache.
At the best situation (we’ve guessed the prefetch address correctly), the latency of accessing a data from SDRAM will be shortened to 2 CYCLES.

## Slide 19: Simulation
FIR + MM + QSORT
Compile optimization: O3
mprj == AB00_0000
  Calculation start
mprj == AB10_0000
  Calculation finish

## Slide 20: Result (Hardware)
(1) Setup: 2.93 ms
(2) Calculation: 4.81(fir) - 0.98(uart) + 2.95(mm) - 0.97(uart) + 0.77(qs) = 6.58ms
(3) Check answer: 0.68(fir) + 0.24(mm) + 0.62(qs) = 1.54
Original (Lab6)
Our work
(1) Setup: 1.46ms
(2) Calculation: 0.07ms
(3) Check answer: 0.12 ms
Calculation improvement: 9300%
Calculation cycle: 2800
(including sending FIR coefficients, sending DMA configurations, DMA transporting data from SDRAM, calculation of 3 functions, and DMA sending back data to SDRAM)

## Slide 21: Result (UART)
(1) interrupts to trigger ISR : 1
(2) time spent in one ISR : 0.9 (ms) = 36000 (cycles)
Original
Our work
(1) interrupts to trigger ISR : n
(2) time spent in one ISR :
n | time | cycle | cycle / interrupt
2 | 0.48 (ms) | 19200 | 9600
3 | 0.60 (ms) | 24000 | 8000
4 | 0.72 (ms) | 28800 | 7200
5 | 0.85 (ms) | 34000 | 6800