## Slide 1: Synthesis Guide
SOC Design

## Slide 2: Synthesis Guide
We synthesis under【 Vivado GUI 】
You need to select the FPGA for Synthesis
  Follow up the SIM_Workflow to select FPGA Board
  Edit FPGA Board in the project

## Slide 3
0. Select FPGA board
0.1. 左鍵點擊 Tools，並且點擊Settings

## Slide 4
0.2. Modify Project Device
  Select PYNQ-Z2 (xc7z020clg400-1)

## Slide 5
1.1 Add Constraints
1.1.1 Add Sources
  【右鍵點擊Design Sources，選擇Add Sources 】

## Slide 6
1.1.2 Add or Create constraints
  【選取Add or Create constraints】

## Slide 7
1.1.3 Add Files
  【如果已有Constraints，選取Add files】
  【如果沒有Constraints，選取Create file】

## Slide 8
1.2 Modify Clock Constraints
  1.2.1 設定Clock 的Constraints
  create_clock –period period_time –name axis_clk –waveform {Rise_time Fall_time} [get_ports axis_clk]

## Slide 9
1.2.2 Run Synthesis

## Slide 10
1.2.3 Report Timing Summary

## Slide 11
  Export to timing summary file

## Slide 12
1.2.4 Check the Design Timing Summary
  Slack time has to be positive integer

## Slide 13
1.2.5 Edit Timing Constraints
  If there is negative slack time, you need to increase timing constraints

## Slide 14
  Edit the axis_clk constraints, then re-run the timing summary.