## Slide 1: FIR Workbook (lab_3)
SOC Design
Revise: 7-8-2024
- Elaborate more on testbench function
- Write one to clear ap_done

## Slide 2: Function specification
Same as course-lab_2(FIRN11stream)
y[t] = Σ (h[i] * x[t - i]）

## Slide 3: Design specification
TBD – Based on size of data file

## Slide 4: You will implement - fir.v - fir_tb.v (testbench – you can reference and modify from Github fir_tb.v) Lab Github: https://github.com/bol-edu/caravel-soc_fpga-lab/tree/main/lab-fir

## Slide 5: FIR module interface (AXI-Lite, AXI-Stream)
AXI-lite:
  https://www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081
  https://docs.xilinx.com/r/en-US/pg202-mipi-dphy/AXI4-Lite-Interface
AXI-stream:
  https://developer.arm.com/documentation/ihi0051/latest/
  https://docs.xilinx.com/r/en-US/pg256-sdfec-integrated-block/AXI4-Stream-Interface
BRAM Interface: Synchronous read/write

## Slide 6: AXI4-Lite Read Transaction

## Slide 7: AXI4-Lite Write Transaction

## Slide 8: AXI4-Stream Transfer Protocol

## Slide 9: Data Transfer Handshake : TVALID, TREADY
TVALID asserted before TREADY
TREADY asserted before TVALID
TVALID and TREADY asserted simultaneously
For a transfer to occur, both TVALID and TREADY must be asserted
A Transmitter is not permitted to wait until TREADY is asserted before asserting TVALID
Once TVALID is asserted, it must remain asserted until the handshake occurs
A Receiver is permitted to wait for TVALID to be asserted before asserting TREADY

## Slide 10: SRAM Access Timing
x
x
x
x
x
x
x
x
Write data is written when WE/EN is sampled
Read data is available in next cycle, when EN is sampled
SRAM access has different modes, refer to https://docs.xilinx.com/r/en-US/am007-versal-memory/Read-Operation?tocId=VRYu0HURA1U147fufYDMNQ

## Slide 11: Deliver module header
The I/O signals are listed in fir.v.
You are requested to use simplified AXI-lite and AXI-stream protocol.

## Slide 12: Configuration Register Access Protocol

## Slide 13: Configuration Register Address map
Address
0x00 – [0] - ap_start (r/w)
set when ap_start signal assert
reset, when start data transfer, i.e. 1st axi-stream data come in
[1] – ap_done (ro) -> when FIR process all the dataset, i.e. receive tlast, and last Y is generated and transferred
[2] – ap_idle (ro) -> indicate FIR is actively processing data
0x10-14 - data-length
0x20-FF – Tap parameters, (e.g., 0x20-23 Tap0, 0x24-0x27 Tap1 .. in sequence …)
Note: Tap parameters set at 0x80 can use lower address bit directly for SRAM address.

## Slide 14: ap_start protocol and implementation
ap_start is a read/write registers
When ap_start is programmed one, the FIR engine starts.
Host Software or testbench can program ap_start
  When ap_idle is one.
  After data-length, tap parameters are programmed
  If ap_start is programmed one when ap_idle is zero (i.e. engine is running), the ap_start is not effective
ap_start is set by software/testbench, and reset by engine
Engine resets ap_start when engine is not idle, i.e. engine starts processing data

## Slide 15: ap_done protocol and implementation
It is read/write-one-clear register
ap_done is reset in the following condition
  Reset signal is asserted
  After a task complete, the ap_done is cleared by
    When ap_done is read, i.e. address 0 is read
    Write one to ap_done register bit to clear
    => Choose one implementation
ap_done is asserted when engine completes last data processing and data is transferred

## Slide 16: ap_idle protocol and implementation
ap_idle is set to 1 when reset
ap_idle is set to 0 when ap_start is sampled
ap_idle is set to 1 when FIR engine processes the last data and last data is transferred

## Slide 17: Handle Configuration read/write while engine is active
It is illegal operation, but we still need to handle it.
Cfg read: TapRAM read return ‘hffffffff (invalid value, software can check), other address, return valid value
Cfg write: ignore, illegal action

## Slide 18: Testbench Specification

## Slide 19: Testbench
fir_tb(Please name your top module same as fir for simulation)
The testbench should keep in the same directory with Makefile
Block-level Protocol (ap_start, ap_done):

## Slide 20: Host software / Testbench Programming Sequence
Check FIR is idle, if not, wait until FIR is idle
Program length, and tap parameters
Program ap_start -> 1
Fork
  Transmit Xn,
  Receive Yn
  Polling ap_done
When ap_done is sampled, compare Yn with golden data
Wait for ap_start
Set ap_idle = 0
Process data
If reach data-length, set ap_done
Host Software / Testbench
FIR Engine
Note: Transmit Xn (stream-in), Receive Yn (stream-out) and Polling ap_done (axilite) are running concurrently. They are using different interface and do not interfere each other

## Slide 21: Testbench – Develop your own testbench
Setup phase
  Load datafile, and count # of data = data_length
  Program tap_parameters and data_length, read back and check it is correctly programmed
  Compute Yn expected value, or load golden data into Yn buffer
  Read and check ap_start, ap_idle, ap_done are in proper state
Execution phase
  Program ap_start
  Start latency timer
  Fork the following operations, run concurrently
    Task1(axis-in): Stream_in_Xn
    Task2(axis_out): Stream_out_Yn and save into Yn buffer
    Task3(axilite):
      Polling ap_done, when ap_done is sampled, disable tasks (stream_in_Xn, stream_out_Yn, and Polling)
      Read/write tap_parameters: make sure it does not corrupt fir computation
        Read return invalid value, e..g. ‘hffffffff
        Write ignored
Checking Phase
  Report latency
  Compare Yn buffer with golden data
Repeat 2 – 3 for three times
Note: You may print message to assist debugging

## Slide 22: TestBench – Axilite write
Axilite write
  Spawn two processes: aw_proc, w_proc
  Each process has random initial delay 0 – 5T
    Asserts awaddr (wdata) when awvalid (waddr) asserts
    Wait for awready (wready)
    Once awready (wready) is sampled active, invalidate awaddr (wdata)
    Optionally wait for bvalid ( in our case, no bvalid)

## Slide 23: TestBench – Axilite read
Axilite read
  Spawn two processes: ar_proc, r_proc
  Each process has random initial delay 0-5T
    Asserts araddr, and rready
    Once arready is sampled active, invalidate araddr
  Check rvalid is only asserted after arvalid and arready are asserted

## Slide 24: TestBench – axi-stream X input
Protocol
  For a transfer to occur, both TVALID and TREADY must be asserted
  A Transmitter is not permitted to wait until TREADY is asserted before asserting TVALID
  Once TVALID isasserted , it must remain asserted until the handshake occurs
  A Receiver is permitted to wait for TVALID to be asserted before asserting TREADY
Testbench
Randomize tvalid initial delay
  Case1: short latency [0-1]
  Case2: long latency [0-2 x Filter latency]
Once sampled tready, deasserts tdata

## Slide 25: Testbench: axi-stream Y output
spawn a task ->task_sm_tready
  randomize sm_tready delay
    Short latency: delay [0-5]
    Long latency: delay [0- 2* filter latency]
  when both sm_tready and sm_tavlid sampled asserted,
    Check data
    finish the task
Note: sm_tready could be asserted before sm_tvalid asserted

## Slide 26: Test dataset
Samples_triangular_wave.dat
out_gold.dat

## Slide 27: SRAM Interface Implementation
Refer to verilog-sram.pdf - Use memory for ASIC flow
Github updated - https://github.com/bol-edu/caravel-soc_fpga-lab/tree/main/lab-fir
Implement SRAM without .db/.lib
Use external SRAM (bram.v). fir.v provides ports to interface with the external SRAM. So, the fir.v can be synthesized with BRAM
Two size of bram.v ( you choose either one to fit your design)
  bram11.v (11 x 32) – depth 11
  bram12.v (12 x 32) – depth 12
fir
axilite
axis_slave (Xn)
axis_master(Yn)
tap_RAM
data_RAM

## Slide 28: Submission (1/2)
Hierarchy:
  StudentID_lab3/
    Waveform
    Simulation.log
    Report.pdf
    Synthesis report
    Github link
Your Github link should attach the file
  fir.v （the fir design）
  fir_tb.v ( the testbench )
  Log files including : synthesis, simulation, static timing report
  Synthesis report – area usage, Including FF, LUT (Note: there should be no BRAM because BRAM is an external model, not in the RTL design)
  Timing Report, including slack, and max delay path
  Waveform – show
    Configuration write
    ap_start, ap_done ( measure # of clock cycles from ap_start to ap_done)
    Xn stream-in, and Yn stream-out
  Report
Location of design (If use vivado to design)
  hostproject/hostproject.srcs/sources_1/new/

## Slide 29: What is included in the report
Block Diagram
  Datapath – dataflow
  Control signals
Describe operation, e.g.
  How to receive data-in and tap parameters and place into SRAM
  How to access shiftram and tapRAM to do computation
  How ap_done is generated.
  …..
Resource usage: including FF, LUT, BRAM
Timing Report
  Try to synthesize the design with maximum frequency
  Report timing on longest path, slack
Simulation Waveform, show
  Coefficient program, and read back
  Data-in stream-in
  Data-out stream-out
  RAM access control
  FSM

## Slide 30: Submission (2/2)
Compress all above files in a single zip file named
  StudentID_lab3.zip (e.g., 111061545_lab3.zip)
Submit to NTHU eeclass
Deadline:
  ‐ 20% off for the late submission penalty within 3 days

## Slide 31: Supplement

## Slide 32: Use Memory in ASIC Flow

## Slide 33: Memory Inference in ASIC
ASIC Synthesis tool does not infer memories from RTL in the way FPGA synthesis tools do.
Use Memory Compiler
  Generate memory block with the specification (bitwidth, depth, # of port)
  (.lef) – Library Exchange Format – containing placement information
  Schematic & Netlist (for LVS and functional verification)
  (.v) Function model (verilog) with timing check – for RTL simulation and gate-level simulation
  (.lib/.db) – Liberty Timing File – containing Timing delay Dynamic/Static timing analysis, and synthesis
  (.gds) – Graphical Database System – containing final layout information
In RTL code, explicitly instantiate the memory, and design its control signals, e.g. Enable, read/write, address, input/output data

## Slide 34: Note on ASIC Implementation with SRAM
RTL design use memory instance directly. Need to provide sram synthesis library, either .lib, or .db (synospsy design-compiler). There is no particular inference method. (note: Xilinx FPGA can use inference)
If there is no sram .lib, or .db, you may put the sram outside using module ports. In this case, you can simulate with post-synthesis gate with sram behavior model. To get sram interface timing optimization, you will need to specify sram interface timing constraints, for example, output delay, input delay.

## Slide 35: SRAM with .db/.lib
RTL Simulation
  RTL code with instance of SRAM
  Simulate with functional model
Synthesis
  Refer to .lib for SRAM timing/area information
  Optimize timing for SRAM interface timing
Post-Synthesis Gate-level Simulation
  Post layout gate-level timing simulation
  Use functional model with timing check (specify/endspecify)
// RTL module
module your_design( …) begin
// instantiate SRAM
SRAM32X32 (CLK, WE, EN, ADDR, DI, DO)
endmodule
// Functional Model with timing check
module SRAM32X32( … ) begin
specify // timing check
endspecify
end
// Timing model : .lib

## Slide 36: SRAM without .lib/.db
SRAM instance could not be in RTL design for synthesis, instead, provide ports to interface with SRAM
RTL simulation
  Simulate with SRAM model
Synthesis
  Provide timing constrains (e.g. output delay, input delay ) for SRAM interface ports
Post Synthesis with gate-level simulation
  Simulate with SRAM functional model with timing check
// RTL module
module your_design(
// SRAM interface ports
SRAM_EN,
SRAM_ADDR,
…) begin
// No SRAM instance
// SRAM32X32 (CLK, WE, EN, ADDR, DI, DO)
endmodule
// Functional Model with timing check
module SRAM32X32( … ) begin
specify // timing check
endspecify
end

## Slide 37: Timing Check Tasks in Verilog
Specify block can be used to specify setup and hold times for signals
  specify and endspecify (Use specparam to define parameters in specify block)
$setup (data, clock edge, limit)–Displays warning message if setup timing constraint is not met
  $setup(d, posedge clk, 10)
$hold (clock edge, data, limit)–Displays warning message if hold timing constraint is not met
  $hold(posedge clk, d, 2)
$width (pulse event, limit)–Displays warning message if pulse width is shorter than limit
  $width(posedge clk, 20) –specify start edge of pulse
$period (pulse event, limit)–Check if period of signal is sufficiently long
  $period(posedge clk, 50)

## Slide 38: Specify Block Example

## Slide 39: SRAM Access in behavior model and Synthesizable Hardware Design ref : spiflash-vip.v v.s. spiflash.v

## Slide 40: Example: spiflash design
spiflash-vip.v - spiflash behavior model
  access sram as an model
bram.v – BlockRAM behavior model
spiflash.v
  Adapt from spiflash-vip.v, synthesizable verilog design
  Generate bram interface signal to access data
  Reference code:
  https://github.com/bol-edu/caravel-soc_fpga-lab/tree/main/spiflash

## Slide 41: SRAM Access Timing
x
x
x
x
x
x
x
x
Write data is written when WE/EN is sampled
Read data is available in next cycle, when EN is sampled
SRAM access has different modes, refer to https://docs.xilinx.com/r/en-US/am007-versal-memory/Read-Operation?tocId=VRYu0HURA1U147fufYDMNQ

## Slide 42: BRAM Model
module bram #( parameter FILENAME = "firmware.hex")
(
input wire CLK;
input wire [3:0] WE0;
input wire EN0;
input wire [31:0] Di0;
output reg [31:0] Do0;
input wire [31:0] A0
)
reg [7:0] RAM[0:4*1024*1024-1]; // Declare Memory Storage
always @(posedge CLK)
if(EN0) begin
Do0 <= {RAM[{A0[31:2],2'b11}],
RAM[{A0[31:2],2'b10}],
RAM[{A0[31:2],2'b01}],
RAM[{A0[31:2],2'b00}]} ;
if(WE0[0]) RAM[{A0[31:2],2'b00}] <= Di0[7:0];
if(WE0[1]) RAM[{A0[31:2],2'b01}] <= Di0[15:8];
if(WE0[2]) RAM[{A0[31:2],2'b10}] <= Di0[23:16];
if(WE0[3]) RAM[{A0[31:2],2'b11}] <= Di0[31:24];
end
else
Do0 <= 32'b0;
initial begin
$display("Reading %s", FILENAME);
$readmemh(FILENAME, RAM);
$display("%s loaded into memory", FILENAME);
$display("Memory 5 bytes = 0x%02x 0x%02x 0x%02x 0x%02x 0x%02x",
RAM[0], RAM[1], RAM[2], RAM[3], RAM[4]);
end
@(posedge CLK) if EN0 is sampled, output its memory content to Do0
@(posedge CLK) if WE[3:0] is sampled, RAM is written with Di0 per byte

## Slide 43: spiflash-vip – behavior model to access RAM
reg [7:0] memory [0:16*1024*1024-1]; // 16MB
initial begin // memory content loaded data from file
$readmemh(FILENAME, memory);
end
Memory defined and initialization
buffer = memory[spi_addr]; // memory read
Memory data is available the same time address is supplied. This is not feasible in the actual memory system.
memory[spi_addr] = buffer;
memory write access
memory read access

## Slide 44: spiflash.v – Synthesizable hardware design
Generate SRAM interface signals
  Addr, EN, WEN, Din, Dout
  The interface signal is generated from internal control logic (FSM) Interface signals follows the interface timing specification, e.g. read data is available in next clock cycle
BRAM RAM
Addr
EN
WEN
Din
Dout
Clk
Rst
// BRAM Interface
assign romcode_Addr_A = {8'b0, spi_addr};
assign romcode_Din_A = 32'b0;
assign romcode_EN_A = (bytecount >= 4);
assign romcode_WEN_A = 4'b0;
assign romcode_Clk_A = ap_clk;
assign romcode_Rst_A = ap_rst;
wire [7:0] memory;
assign memory =
(spi_addr[1:0] == 2'b00) ? romcode_Dout_A[7:0] :
(spi_addr[1:0] == 2'b01) ? romcode_Dout_A[15:8] :
(spi_addr[1:0] == 2'b10) ? romcode_Dout_A[23:16] :
romcode_Dout_A[31:24] ;