## Slide 1: Advanced SOC Design Lab catapult
Jiin Lai

## Slide 2: Catapult
High-level synthesis (HLS) creates RTL implementations from abstract specifications described with C / C++.

## Slide 3: Tool setup
You need to setup Catapult and Questasim in IC lab account.
  Run “run_catapult” to check the tool is correctly installed.
You also need to setup the directory of some environment variables to run up our sample code.
  Run “lab1_fir” to check the environment variables is setup correctly.
  You may need to create “bin” folder to save execution file.
TA will give you another tool setup guide for tool setup.

## Slide 4: Content
In this lab, we will provide the example code of lab1_fir and part of Lab2_edgedetect_fisc .
Lab1_fir is for you to understand how to use catapult.
Lab2_edgedetect_fisc needs rewrite the code to meet the spec.
  Note: we will provide you a sample code in 01_edgedetect.

## Slide 5: 01_edgedetect block design

## Slide 6: 01_edgedetect

## Slide 7: Lab work

## Slide 8: Lab work - Few Modifications of Original EdgeDetect
Process four pixels per clock cycle.
  Change input data type to compress four 8-bit pixels data read in one read cycle.
Use sum of absolute difference (SAD) for edge magnitude calculation.
  Originally, we use square root in sample code.
Add two crc32 calculation on image input / output.
  We will provide you the crc32 code, you need to use it in your design.
Select the output source from input image or the calculated magnitude.
  Add mux on the top of design.
Remove the angle calculation.
Integrate your edge detect into FSIC
About four pixels per clock cycle, you can check the file “hls_bluebook.pdf” page 102.

## Slide 9: Modified top design in 02_edgedetect_fsic (for your reference)

## Slide 10: Integrate to FSIC

## Slide 11: Integrate to FSIC

## Slide 12: Integrate to FSIC

## Slide 13: Integrate to FSIC

## Slide 14: Provided Content
All content of lab1_fir(walkthrough, mem_ifc, multi_blks)
lab2_edgedetec_fsic
  All content of 01_edgedetect
  Only provide the testbench of 02_edgedetect_fsic, you need to modify the code of 01_edgedetect to satisfy specification.
  crc32.cpp can be accessed by github, which should be used in your design
  https://github.com/bol-edu/caravel-soc_fpga-lab/tree/main/catapult_hls
  03_fsic_prj, after you generate the rtl design of 02_edgedetect_fsic, integrate it to FSIC and save all design into this folder.
Note: This lab didn’t need to do synthesis, only need simulation.

## Slide 15: Submission
Please submit the following files to {NTHU eeclass / NTU COOL / NYCU E3}
  hls code of 02_edgedetect_fsic
  Testbench (no matter you modify it or not)
  Synthesis report of hardware design
    Screen shot of table in catapult (including general, run time, memory usage, timing, and area score)
    The file of rtl report (rtl.rpt)
  Questasim simulation result
  tcl file generate by catapult (directives.tcl)
  Integrate to FSIC (rtl design and testbench, we can use these file to execute simulation)
  Simulation result of FSIC
  report_StudentID.pdf
  Github_link.txt
Note: Since the authorization of these lab content, don’t upload the file which is not mentioned above.

## Slide 16: Report
How you design your work
What’s the test result of catapult design(C design checker, testbench)
How to integrate your design in FSIC
What’s the simulation result of FSIC